## Slide 1
EMBEDDED SYSTEMS • EDGE AI • BIOMETRICS
Edge-AI Smart Access Control
Real-Time Face Recognition on STM32H7 via TFLite Micro & FreeRTOS
480 MHz
Cortex-M7
380 KB
INT8 MobileNetV1
On-Device
Zero Cloud
Metin Irkıçatal • Anıl Arda
Bare-metal firmware · TFLite Micro · FreeRTOS · Metric learning

## Slide 2
PROBLEM STATEMENT
The Vulnerability of Cloud Biometrics
Three structural weaknesses make cloud-routed biometrics unfit for mission-critical access control.
Network Latency
Cloud round-trips introduce unpredictable delays — unacceptable for real-time access decisions at the door.
Dependency Failures
A network outage takes the entire system offline — intolerable for hospitals, labs and industrial facilities.
Data Privacy Risks
Shipping biometric templates off-device exposes them to interception and breaks KVKK / GDPR compliance.
Edge-AI Smart Access Control • STM32H7
2 / 16

## Slide 3
OUR APPROACH
The Secure Edge Solution
100% On-Device
All capture, inference and decision logic run inside the STM32H743ZI — no external network call at any stage.
Deterministic Execution
Inference runs in hardware with bounded, predictable latency.
Privacy by Design
All biometric data is confined to local memory — never leaves the chip.
Cost & Energy Efficient
Orders of magnitude leaner than PC or GPU-class solutions.
Ultimate Reliability
Functional during full network blackouts — no dependency on the cloud.
Edge-AI Smart Access Control • STM32H7
3 / 16

## Slide 4
SPECIFICATION
Defining the System Requirements
Functional Requirements
1
Accept 96×96 grayscale frame injection
2
Run the TFLite Micro inference pipeline locally
3
Emit Accept / Reject decision via GPIO & UART
4
Maintain deadlock-free FreeRTOS scheduling
Non-Functional Requirements
1
End-to-end latency < 500 ms per frame
2
Total Flash ≤ 2 MB / Total SRAM ≤ 1 MB
3
INT8 quantized model < 300 KB
4
FAR < 5% & FRR < 10%
Edge-AI Smart Access Control • STM32H7
4 / 16

## Slide 5
TRAINING DATA
Expanding the Dataset via Augmentation
The Challenge. The AT&T Face Database carries limited variation per subject, creating a high risk of model overfitting.
Rotation Matrix
Synthetic rotation produces angle-tolerant variants.
Bounding-Box Crop
Systematic crops widen the framing distribution.
Contrast Shift
Lighting changes simulate real-world illumination.
Impact. Synthetic diversity lets the model generalize across head poses without millions of raw photos — keeping training cheap and the dataset on-task.
Edge-AI Smart Access Control • STM32H7
5 / 16

## Slide 6
MODEL DEVELOPMENT
Transfer Learning: Fine-Tuning the Final Layers
Frozen Base Layers (Feature Extraction)
Trainable Head
Re-trained on the augmented set
01
Leverage the Pre-trained Backbone
MobileNetV1 weights from ImageNet stay frozen — we keep the heavy convolutional features and skip the expensive training they would normally require.
02
Train Only the Final Layers
The new head learns face-specific representations on our augmented set, adapting the network with a fraction of the compute and data.
Edge-AI Smart Access Control • STM32H7
6 / 16

## Slide 7
MODEL DEPLOYMENT
Quantization & Flashing the Updated Model
1
Optimize
INT8 post-training quantization shrinks the fine-tuned model below 300 KB while preserving accuracy.
2
Compile
The quantized model is converted to a C byte-array, ready to embed directly into firmware.
3
Flash
Model + pre-computed reference embeddings are written to the STM32H7 internal Flash — fully self-contained.
Result. The board is now completely standalone and intelligent — every byte of intelligence sits in on-chip Flash, no external dependency at runtime.
Edge-AI Smart Access Control • STM32H7
7 / 16

## Slide 8
FIRMWARE ARCHITECTURE
The FreeRTOS Deterministic Pipeline
T1
Frame Capture
Priority: Highest
DMA interrupt grabs a 96×96 frame.
→
T2
Preprocessing
Priority: High
INT8 normalization + tensor pack.
→
T3
Inference
Priority: Lowest
TFLite Micro runs the network.
→
T4
Access Control
Priority: High
GPIO + UART emit the decision.
Deterministic Scheduling Constraints
T1 holds the highest priority — DMA interrupts are serviced immediately.
T3 (neural net) holds the lowest priority — heavy compute can never starve time-critical capture.
Tasks are linked sequentially through semaphores and queues — deadlock-free by construction.
Edge-AI Smart Access Control • STM32H7
8 / 16

## Slide 9
INFERENCE STRATEGY
Metric Learning: Cross-Similarity Inference
We don't classify — we compare.
The TFLite Micro network acts as a feature extractor. Its penultimate layer outputs a unique numerical embedding for every face it sees.
We measure the cosine similarity between the live embedding and reference embeddings stored in Flash. A high similarity = a biometric match.
New users are enrolled by storing a fresh reference vector — no model retraining required.
Cosine Similarity
Reference vector
Live vector
θ
small θ → high cos(θ) → match
Edge-AI Smart Access Control • STM32H7
9 / 16

## Slide 10
HARDWARE BRING-UP
From Theory to Practice: Hardware Transition
YESTERDAY / VIRTUAL
Renode Simulation
Memory-mapped virtual environment exposed UART and ST-LINK without real electrical interfaces — letting us build and prove the firmware stack purely in software.
TODAY / PHYSICAL
STM32H743ZI Board
The same firmware now runs on real silicon — bare-metal, no HAL, direct register access. The transition validates that our software works in both simulated and physical environments.
Edge-AI Smart Access Control • STM32H7
10 / 16

## Slide 11
COMMUNICATION LAYER
UART & Frame Protocol Design
Sync Pattern
0xAA 0x55 0xAA 0x55
4 B
Length
9216
2 B
Payload
96 × 96 grayscale
9216 B
CRC-16
CCITT-FALSE
2 B
Total frame → ~9224 B • bare-metal uart.c & frame_proto.c drivers
Error Recovery
A 4-byte sync-pattern hunt re-locks the receiver after any framing slip — no permanent loss of sync on the wire.
Integrity
CRC-16/CCITT-FALSE validates every payload — only loss-free frames reach the TFLite Micro engine.
Edge-AI Smart Access Control • STM32H7
11 / 16

## Slide 12
WHAT CHANGED
Architectural Comparison: Virtual vs. Real Hardware
System Component
Renode (Virtual)
STM32H7 (Real Hardware)
Camera I/O
Memory-mapped virtual sensor
16 KB interrupt-based UART RX ring buffer
Output Logging
Virtual terminal log
Physical GPIO + PC-parseable [RESULT] frames
System Clock
Cycle-accurate virtual clock
64 MHz HSI clock (real silicon)
Interrupt Control
Simplified virtual NVIC
Full 166-entry vector table via startup.s
Edge-AI Smart Access Control • STM32H7
12 / 16

## Slide 13
VALIDATION
Real-World Test Automation: Python Host
Python Host
AT&T dataset reader
UART @ 115200
STM32H7
Returns [RESULT] flags
Image Pipeline
Reads PGM images on the fly and rescales them to the 96×96 format expected by the board.
Protocol Framing
Wraps each frame with the sync header, length, payload and CRC required by the firmware.
Batch Testing
Streams frames from 40 subjects, parses the [RESULT] tags, computes FAR / FRR on real hardware.
Edge-AI Smart Access Control • STM32H7
13 / 16

## Slide 14
MEASUREMENTS — 64 MHz SNAPSHOT
Hardware Performance & Resource Utilization
622 KB
Flash usage
30% of 2 MB
Holds the INT8 model and the entire FreeRTOS firmware. Well below capacity.
395 KB
SRAM usage
38% of 1 MB
Includes the 16 KB UART RX buffer and the 2048-word inference stack. Plenty of headroom.
37 ms
AI inference
@ 64 MHz
Already excellent at low clock. Expected to drop to ~5 ms at 480 MHz PLL.
Today's bottleneck. End-to-end time is dominated by the ~800 ms UART transfer at 115 200 baud — not compute. The next slide attacks exactly that.
Edge-AI Smart Access Control • STM32H7
14 / 16

## Slide 15
Edge-AI Smart Access Control • STM32H7
01
Clock Bring-up
Migrate from the 64 MHz HSI to the 480 MHz PLL via VOS0 voltage scaling. Inference target drops to ~5 ms, exposing the data-transfer wall as the next limiter.
02
DMA-based Comms
Replace interrupt-driven UART RX with DMA + idle-line detection. CPU is fully bypassed during transfer, eliminating per-byte overhead.
ROADMAP
Future Steps:
Maximum Performance Optimization
Target. End-to-end latency below 500 ms with zero CPU overhead on UART reception.

## Slide 16
Thank you.
Questions are welcome.
TFLite Micro
FreeRTOS
STM32H7 — bare-metal
Metin Irkıçatal • Anıl Arda